## Slide 1: Survival Programming
What you need when your client is unprepared…

## Slide 2: Your contract AIA form OAB101
Schematic Design (SD) 15%
Design Development (DD) 20%
Contract Documents (CD) 40%
Bidding and Negotiation (BN) 5%
Contract Administration (CA) 20%

## Slide 3: There’s no programming in your contract..
The Program is a document of needs, which documents
  Goals
    Might be financial, functional, performative, marketing/image or all of the above
  Requirements
    Might be a general listing of the rooms or a complete manual of the people and their needs for movement, storage, systems,
  Resources
    Might just be who to call at the building inspector’s or a detailed set of codes, standards, and vendors

## Slide 4: How to proceed when the client has no program
Study: the building type, the site type, the organization type to get the big parts that are typical in mind, and the terminology at your fingertips (for a more informed discussion)
Listen: to what your client is saying…what is their reason to be? What dreams? What nightmares? How chaotic is the place they have?
Look: for signs they are adapting to their current locations, overflows, worn carpets (critical paths) piles of paper, watch a day in their life
Think: begin combining what you’ve studied with what you’re seeing and hearing…restate what you hear to them “so my understanding is…”
Ask: about what you don’t know. NEVER assume you know more then the owner…especially about their business…

## Slide 5: When you visit
Be prepared, have your case studies DONE!
Know their terminology
Eyes open! Pay attention to their culture, where is wear and clutter?
Ears open! Pay attention to noise processes/machines, people struggling to pay attention
Document it all! In video and stills and notes and sketches

## Slide 6: Go Home
Organize your video and images
Make notes RIGHT AWAY about what you saw and thought
Go to sleep

## Slide 7: Begin the program…restate the goals
Write a goal statement based on what you heard the owner say
  “The reason we need this new building is for more Sunday school rooms”
  “The reason we’re doing this is to be able to recruit and get the most out of the best people we can hire”
  “The reason we’re doing this is to make a 35% return on investment before the fourth year closes”
  “We need this new building to keep growing, we’ve grown 20% a year for ten years now”

## Slide 8: Goal components
What the group’s reason to be is
What the primary reason for the project is
What the secondary reason’s for the project are
These are ideas, not numbers
(remember these are the owners goals, not yours, you MUST write your own as well!)

## Slide 9: Objectives follow goals
Objectives are the tactics you’ll use to achieve a goal
  “We need to show we are environmental leaders”
    Employ LEED platinum standards in the design, purchasing, construction and operation of the building.
    Meet 2030 challenge for zero carbon in energy production
    Use no potable water for irrigation, toilets, or cooling

## Slide 10: Criteria lets you measure
Criteria are the way you measure the performance towards a goal
  Did the project score enough LEED points to hit Platinum?
  Are we producing more energy than we consume?
  Is the potable water consumption 50% less than a comparable building?

## Slide 11: Now…Make a list
List EVERY space the project needs
  Who “lives” in it?
  Who uses or visits it?
  What furniture do they have?
  What equipment do they have?
  What adaptations have they made?

## Slide 12: Check it twice
What did you leave out?
  Toilets?
  Custodial spaces?
  Equipment/mechanical/electrical/telcom/alarm/sprinkler spaces?
  Dumpster space?
  Delivery?
  Rooftop spaces?

## Slide 13: Open a separate file for each list item
Make a page template
  Room name
  Primary user, secondary users
  Time of use, duration,
  Critical adjacencies (direct, indirect, visual conn)
  Desired solar exposure, desired lighting strategy
  Degree of privacy (visual, acoustical, access)
  What height should it be?
  What character? Formal? Informal? Utility?
  Contents (furniture, built-ins and equipment) Draw to scale, leave space for moving around (and wheelchairs!)
  Draw a line around it…what is the minimum width that’s possible, the minimum length?
  List the area (length x width) in the lower right corner of the page

## Slide 14: Sum each up
Write a summary page
List each room, and the area of each room
Make sure to account for systems spaces
Total it up at the bottom (you multiply this times the cost per square foot (from r.s. means) to begin talking to the owner about budget)
Talk dollars early to avoid anger!

## Slide 15: Once the owner is ready…
Budget talk might be stressful
Let the owner talk to you about their comfort with the number
Remember, most estimates are only for the building, not FF&E (fixtures, furnishings, and equipment)
VERY IMPORTANT (include the contingency line item in your estimate!) Allow 15% at this stage for new const, 25% for remodeling, tighten the number as the number of unknowns decreases

## Slide 16: So now you know…
What the reason for the project is
What the reason for the owner’s existence is
Now you can show them how to conceptualize it to put those two things together.
Concept=Reason for project x reason for existence

## Slide 17: Now…5 in 60
Now you know what you need to begin design concepts
Make 5 alternative models at 1”=20’ scale
Begin!
…due at 5:30 p.m. today….